## Slide 1: EASAC workshop at the Royal Academy , Stockholm, Sept. 19-20
Wind Energy Systems – Present Status and Ecobalances
Hermann-Josef Wagner
Institute for Energy Systems and Energy Economy
Ruhr-University Bochum, Germany
lee@lee.rub.de

## Slide 2: Structure of my presentation
Present status of wind energy use
Cumulated Energy and Ecobalances
Results of the wind park alpha ventus

## Slide 3: Electricity from wind energy
Source: Global Wind Satistics; Global Wind Energy Council, www.gwec.net,
Status 10 Feb. 2013
Status of installed wind power |  | 
 | Rated Capacity End of 2012 [GW] | Share worldwide [%]
China | 76 | 27
USA | 60 | 21
Germany | 31 | 11
Spain | 23 | 8
India | 18 | 6
Italy | 8 | 3
Great Britain | 9 | 3
France | 7 | 3
Canada | 6 | 2
Portugal | 5 | 2
Remaining countries | 40 | 14
Total | 283 | 100

## Slide 4: Structure of my presentation
Present status of wind energy use
Cumulated Energy and Ecobalances
Results of the wind park alpha ventus

## Slide 5: Example of Process-Chain-Analysis
Final Product:
Aluminium Component
Notes: Nicht nur Energieträger betrachten sondern auch andere Materialien, z.B. Stah
Diversifizierung allein kann aber nicht ausreichend sein zur Betrachtung, Beispiel isländische Energieversorgung.

## Slide 6: Process chain for final energy carrier
Example: Overall Efficiencies of Supply for final energy carrier
Problem: different forms of energy must be made comparable.
Electricity, oil-products, etc. are count back on primary energy with typical (country-specific) process chains.
The primary energy equivalent of electricity is 2,90 kWh (Overall Efficiencies of Supply gel).
  Overall Efficiencies of Supply:
The primary energy equivalent of oil is 1,13 kWh (Overall Efficiencies of Supply goil).
Comment:
If there are enough information, you can devide the primary energy equivalent in a fossil, regenerative and nuclear share.

## Slide 7
Source: Nordex AG
Assembling of a wind converter by Nordex AG
Notes: 7
7

## Slide 8
© Doti 2009
Montage of an cabin - windpak alpha ventus
Notes: 8

## Slide 9: Structure of my presentation
Present status of wind energy use
Cumulated Energy and Ecobalances
Results of the wind park alpha ventus

## Slide 10: Planned offshore windparks and cable lines in Germany (North Sea, beginning of 2011)
The dark yellow projects are in operation (alpha ventus was the first), the soft yellow projects should be go in operation until 2014

## Slide 11: Windpark alpha ventus
© Doti 2009

## Slide 12: Life Cycle Analysis wind park alpha ventus Reference system
12 Wind energy converter, each 5 MW
(6 of Multibrid and 6 of REpower company)
Operation time 20 years
Lifetime foundation 20 years
Capacity Factor 45% (load duration 3900 h/a): incl. maintenance- and failure times, power consumption of WEC and transmission platform inside wind park
Maintenance and services: Change of 1/2 gearbox per station and operation time Change of 1,25 rotor blades per station and operation time 120 helicopter transports per year for the wind park 180 ship transports per year for the wind park

## Slide 13: Fundaments for windmills for alpha ventus
© Doti 2009
Tripods for the Multibrid windmills
Notes: 13

## Slide 14: Fundaments for windmills for alpha ventus
Jackets for the Repower windmills

## Slide 15: Results production of 1x Multibrid M5000 Material balance
Chart: Including grounding and grid connection 1.826 t
| Eisenmetalle | Nichteisenmetalle | Kunstoffe | Sonstige
 | 0.89264 | 0.01273 | 0.043457 | 0.051169

## Slide 16: Results production of 1x REpower 5M Material balance
Chart: Including grounding and grid connection 1.636 t
| Eisenmetalle | Nichteisenmetalle | Kunstoffe | Sonstige
 | 0.87367 | 0.025691 | 0.051525 | 0.049109

## Slide 17
Results of the wind park alpha ventus
Cumulated Energy Demand(CED) and
Global Worming Potential (GWP)

## Slide 18: Results wind park alpha ventus CED – Life Cycle and use time
Chart: CED Use alpha ventus 471 TJ PE-Equiv.
| Getriebe- wechsel | Rotorblatt- wechsel | Transport und Montage | Ölwechsel | Helikopter- einsätze | Schiffseinsätze
 | 0.063709 | 0.063412 | 0.022304 | 0.030437 | 0.11568 | 0.70445
Chart: CED over life cycle alpha ventus 2.304 TJ PE-Equiv.
| Nutzung | Herstellung | Entsorgung
 | 0.20446 | 0.78361 | 0.011931

## Slide 19: Results wind park alpha ventus GWP – Life Cycle and use time
Chart: GWP over life cycle alpha ventus 149.000 t CO2-Equiv.
| Nutzung | Herstellung | Entsorgung
 | 0.21516 | 0.77276 | 0.012076
Chart: GWP Use alpha ventus 32.000 t CO2-Equiv.
| Getriebe- wechsel | Rotorblatt- wechsel | Transport und Montage | Ölwechsel | Helikopter- einsätze | Schiffseinsätze
 | 0.059746 | 0.062175 | 0.022009 | 0.02078 | 0.1154 | 0.71989

## Slide 20: Results wind farm alpha ventus CED and GWP – Life cycle – by elements
Chart: CED LZ alpha ventus 2.304 TJ PE-equiv.
| 6x Multibrid inkl. Gründung und 30 kV Kabel | 6x Repower inkl. Gründung und 30 kV Kabel | Netzanbindung inkl. Onshore Umspannwerk
 | 0.42606 | 0.39592 | 0.17802
Chart: GWP LZ alpha ventus 149.000 t CO2-equiv.
| 6x Multibrid inkl. Gründung und 30 kV Kabel | 6x Repower inkl. Gründung und 30 kV Kabel | Netzanbindung inkl. Onshore Umspannwerk
 | 0.43044 | 0.40118 | 0.16838

## Slide 21: Example of details: production grid connection
Chart: CED production grid connection (incl. grounding) 409 TJ PE-equiv.
| offshore Plattform | Bestückung offshore Plattform | Seekabel 110kV | Onshore Umspannwerk
 | 0.20272 | 0.090357 | 0.6516 | 0.055321
Chart: GWP production grid connection (incl. grounding) 25.000 t CO2-equiv.
| offshore Plattform | Bestückung offshore Plattform | Seekabel 110kV | Onshore Umspannwerk
 | 0.21467 | 0.12442 | 0.59717 | 0.06374

## Slide 22: Energy Payback Time (EPT)
=
+
+
Substituted
fossil energy
Energy supply
for construction, operating
and disposal
Energy Payback Time (EPT):
Notes: Nicht nur Energieträger betrachten sondern auch andere Materialien, z.B. Stah
Diversifizierung allein kann aber nicht ausreichend sein zur Betrachtung, Beispiel isländische Energieversorgung.

## Slide 23: Energy and CO2 Payback Time
Reference System: 12 WEC - Lifetime Foundation 20 a – load duration 3900 h/a – Maintenance: ½ Gearbox, 15 Rotorplates, 120 Helicopter , 180 Ship transports

## Slide 24
Results of the wind park alpha ventus
All considered eco-indicators

## Slide 25: Possible effect-classes and -indicators in Life Cycle Analysis (1)

## Slide 26: Possible effect-classes and -indicators in Life-Cycle Analysis (2)

## Slide 27: Classification of the results Comparison with German Power Mix (uniform ranking)
Chart: Wirkungskategorien
| CED [kWh PE-Eqv./kWh] | GWP [g CO2-Eqv./kWh] | EP [mg PO4-Eqv./kWh] | HTP [g DCB-Eqv./kWh] | POCP [mg C2H4-Eqv./kWh] | AP [mg SO2-Eqv./kWh]
German Power Mix High-Voltage Grid | 5 | 5 | 5 | 4.3319 | 5 | 5
alpha ventus | 0.22745 | 0.23954 | 1.5819 | 5 | 1.262 | 1.1544

## Slide 28: Conclusions
The use of wind energy is worldwide growing
Wind energy is very material intensive → that needs energy
→ emissions
Ecobalances give information about sustainability
The energetic and CO2 payback time for wind parks is about one year and less
Electricity from wind is much more sustainable as electricity from fossils
A sustainability check must be part of every planning of new energy systems

## Slide 29
Thank you for your attention
History Wind mills in the Netherlands

## Slide 30
For Discussion

## Slide 31: Maintenance: Repair of corrosion protection
Photo: Helmut Müller; Sonne, Wind und Wärme 4/2012
This foto was not made in wind park alpha ventus

## Slide 32: Results production 6x Multibrid M5000 Cumulated energy demand
Chart: CED Production Multibrid (6x) Wind farm elements 731 TJ PE-equiv.
| Gründung | Innerpark- verkabelung | WEA
 | 0.59849 | 0.028998 | 0.37251
Chart: CED Production Multibrid (6x excl. Grounding and cable) 272 TJ PE-equiv.
| Turm inkl. Trafo & Umrichter | Gondel | Rotor und Nabe | Transport & Montage
 | 0.42042 | 0.3264 | 0.2347 | 0.018479

## Slide 33: Results production 6x REpower 5M Cumulated energy demand
Chart: CED Production REpower (6x) Wind farm elements 666 TJ PE-equiv.
| Gründung | Innerpark- verkabelung | WEA
 | 0.54635 | 0.031831 | 0.42182
Chart: CED Production WEA REpower (6x excl. Grounding and cable) 281 TJ PE-equiv.
| Turm | Gondel inkl. Trafo & Umrichter | Rotor und Nabe | Transport & Montage
 | 0.31884 | 0.46159 | 0.20202 | 0.017546

## Slide 34: Results production 6x Multibrid M5000 Global warming potential
Chart: GWP Production Multibrid (6x) Wind farm elements 47.000 t CO2-equiv.
| Gründung | Innerpark- verkabelung | WEA
 | 0.60045 | 0.024903 | 0.37465
Chart: GWP Production WEA Multibrid (6x excl. Grounding and cable) 18.000 t CO2-equiv.
| Turm inkl. Trafo & Umrichter | Gondel | Rotor und Nabe | Transport & Montage
 | 0.41634 | 0.32593 | 0.23846 | 0.019274

## Slide 35: Results production 6x REpower 5M Global warming potential
Chart: GWP Production REpower (6x) Wind farm elements 43.000 t CO2-equiv.
| Gründung | Innerpark- verkabelung | WEA
 | 0.55041 | 0.02727 | 0.42232
Chart: GWP Production WEA REpower (6x excl. Grounding and cable) 18.000 t CO2-equiv.
| Turm | Gondel inkl. Trafo & Umrichter | Rotor und Nabe | Transport & Montage
 | 0.31749 | 0.4573 | 0.20682 | 0.01839

## Slide 36
Around 5,600 employees
36,140 students in total
488 doctoral students
2,615 international students
20 faculties
462 million Euros revenue, of which from outside funding 95 million Euros
RUB Research School, funded by the Excellence Initiative of German Government
Ruhr Universität Bochum – Facts